## Slide 1: DESIGN CONTINUED

## Slide 2: Q. Design a computer having 8k of ROM starting at address 0, followed by 8k of RAM. It will also have a memory mapped, bidirectional I/O port at address 8000H. It has 16-bit address bus and 8-bit data bus.

## Slide 3: .

## Slide 4: Q. A computer system with an 8-bit address bus and an 8-bit data bus uses isolated I/O. It has 128 bytes of EPROM starting at address 00H constructed using 128 x 2 chips; 32 bytes of RAM starting at address E0H constructed using 16 x 8 chips; an input device with a ready signal at address 00H; an output device with a READY signal at address FFH; and a bidirectional input/output device with no READY signal at address 80H. Show the design for this system. Include all enable and load logic.

## Slide 5: .

## Slide 6: RELATIVELY SIMPLE CPU

## Slide 7: Contd…
LDAC Instruction LDAC1: DR←M, PC←PC + 1, AR←AR + 1 LDAC2: TR←DR, DR←M, PC←PC + 1 LDAC3: AR←DR, TR LDAC4: DR←M LDAC5: AC←DR
STAC Instruction STAC1: DR←M, PC←PC + 1, AR←AR + 1 STAC2: TR←DR, DR←M, PC←PC + 1 STAC3: AR←DR, TR STAC4: DR←AC STAC5: M←DR

## Slide 8: Execution trace of very simple CPU
Consider the following code segment: 0: ADD4 1: AND5 2: INC 3: JMP0 4: 27H 5: 39H
Initially all registers contain the value 0.

## Slide 9: .

## Slide 10
Design a 16 x 4 memory subsystem with high-order and low-order interleaving using 8 x 2 memory chips for a computer system with an 8-bit address bus.

## Slide 13
Show how the following values are stored in memory in big endian and little endian formats. Each value starts at location 22H. A. 12345678H b. 0927H c. 5551212H

## Slide 15: Assignment
A computer system with an 8-bit address bus and an 8-bit data bus uses memory mapped I/O. It has 32 bytes of ROM starting at address 00H constructed using 32 x 8 chip; 128 bytes of RAM starting at address 80H constructed using 64 x 4 chips; a bidirectional input/output device with no READY signal at address 40H; and an input device with no READY signal at address 60H. Show the design for this system. Include all enable and load logic.